## Slide 1
Zhang Jinyu – zjy@bjtu.edu.cn
School of Computer and Information Technology
SD408
SCC211 Operation System
(Input and Output)

## Slide 2: Objectives
Look at I/O mechanisms
  How we implement access to devices
  Examples based on x86 architecture
Device Drivers
  How we encapsulate I/O functions and manage devices within an Operating System

## Slide 3: Memory Mapped I/O
I/O devices visible as normal memory locations
  Easily accessed using C pointers
考试题
1.将IO看成内存一部分，利用（C语言）指针进行访问
数据总线 8根
地址总线 8根
winxp 32 4G
win 7/10 64 8G

## Slide 4: Isolated I/O
Separate bus for I/O devices
  Easier interfacing: distinct from high-speed memory bus
  Accessed via special instructions
    Generally not supported by compilers (must use assembler)
2. 独立IO线，专门建一条线共CPU访问
高级语言只能访问内存

## Slide 5: Polling or Busy waiting
Code ‘spins’ on busy flag* awaiting status change
  Very wasteful of processor time
Very difficult to interleave useful code
  Need automated mechanism
Also known as Synchronous I/O
* Remember: a flag is just a status bit on device e.g. data available, operation complete, …
轮询：浪费计算机资源
活锁：提高效率，消耗时间
自动化机制
轮到谁，就是谁

## Slide 6: Interrupt Driven/ Asynchronous I/O
发送数据请求，发送中断请求
cpu相应：处理请求
不响应：等待
解决轮询问题
异步，节省时间
不公平，由于优先级更高而不处理中断

## Slide 7: Interrupt Service Routine (ISR)
Note we push a copy of all registers so C handler has access to all system state
Some interrupt systems by default
  Disable interrupts - typically do
  Push all registers - easy but slow
  Push few, if any - fast
必须做
C :control
中断业务历程
不允许其它中断，会把重要信息过滤掉
清空寄存器，留给它用

## Slide 8: Interrupt
If devices share interrupt/ interrupt line
  No idea which generated interrupt
    Back to polling
• After interrupt
  Must poll each device for data ready/ state change
不知道谁发生中断
轮询每一个设备

## Slide 9: Multiple Interrupt Lines
Narrows search when subsequently polling
Groups similar devices
More support required on processor
  Multiple lines/ wires
  Multiple ISRs
缩小搜索范围

## Slide 10: Multiple Interrupt Service Routines
第三个
硬盘
时钟
打印

## Slide 11: Pushal Instruction and C Handler
Pushes x86 registers in following order
struct cpu_registers {
uint32_t edi;
uint32_t esi;
uint32_t ebp;
uint32_t esp;
uint32_t ebx;
uint32_t edx;
uint32_t ecx;
uint32_t eax; };
void C_handler( // Interrupt handler called from assembler ISR
struct cpu_registers regs, uint32_t irq,
uint32_t instr_ptr, uint32_t cs, uint32_t cpu_flags ) {
isr: push $3
pushal
call C_handler …
Always pushed by x86 processor
Interrupt number we pushed ($3)
指令寄存器
执行栈

## Slide 12: Generalizing the Mechanism
Interrupts
  Interrupt Request signal
    Generated by device attached to specific wire/ line
  Message based
    Requested in ‘message’ over intelligent bus, e.g. PCI
Exceptions (can be generic term encompassing others)
  Generated in response to internal processor problem
Software Interrupts
  Initiated by executing special Interrupt/ Trap instruction
发生中断，电压升高
通过互联网
两种：外部，自己
陷阱，设计好的中断

## Slide 13: x86 Exception List
const char * x86Exception[ ] = {
"Division by zero", // 0 F -
"Single step", // 1 FT -
"Non-Maskable Interrupt (NMI)", // 2 I -
"Breakpoint", // 3 T -
"INTO executed with overflow flag set", // 4 T -
"BOUND executed with index outside array bounds", // 5 F -
"Invalid Op-code", // 6 F -
"Device/ Co-processor not available", // 7 F -
"Double fault - no handler for exception", // 8 A 0
"Co-processor Segment overrun (pre i486)", // 9 F -
"Invalid Task State Segment (TSS)", // 10 F E
"Segment not present", // 11 F E "Stack/ Segment Fault", // 12 F E
"General Protection Fault (GPF)", // 13 F E
"Page Fault", // 14 F E
"Exception 0x0F - reserved by Intel", // 15 -
"x87 Floating Point exception", // 16 F
"Alignment check (Ring 3: user mode)", // 17 F 0
"Machine check (internal processor error)", // 18 A ?
"SIMD Floating Point exception", // 19 F -
没有处理
内存管理是分页管理

## Slide 14: Programmable Interrupt Controller
Processor can’t have separate wire to every device
  PC now uses Advanced PIC (Intel 82093 APIC)
Gives priority to most important devices
  Orders generated interrupts
软中断
不能为每一个外设弄一根线
PIC:程序控制器
The PIC is responsible for routing interrupt requests from devices to the appropriate Interrupt Service Routine (ISR) in the system.

## Slide 15: Remapping PIC Interrupts
映射成1个

## Slide 16: Precise and Imprecise Exceptions
Precise Exceptions
  Current instruction(s) complete execution
  Interrupt service routine called
Imprecise Exceptions
  Interrupt service routine called
  Deeply pipelined instructions not fully complete
  Hard to recover from due to unknown state
If unrolled in hardware, leads to complex internal logic
精确的例外
当前指令完成执行
中断服务例程
不精确的例外
中断服务例程
由于未知状态难以恢复．
一级一级执行
没有回滚

## Slide 17: When Exceptions go Wrong
Interrupts MUST be correctly handled
If no interrupt service routine set for interrupt
  Processor raises Double Fault interrupt
  Unknown state can be hard to recover from
    Blue Screen of Death
If double fault isn’t handled
  Processor Triple Faults
  Causes machine restart
二次中断
出现错误但无法处理

## Slide 18: Key feature of Exceptions
Not typically generated by running program*
  Though program could be cause
Allows switch from user to system/ kernel mode
  As x86 has 4 ring levels, need Requested Privilege Level
// Following set for each Interrupt Vector
// Note x86 records more info than just the ISR address
static void set_IDTentry(struct IDTentry * entry, uint32_t address, uint8_t attributes) {
entry->offset = address;
entry->selector= CODE_SEGMENT(1) | GDT | RPL0;
entry->IDTtype_attr = attributes; }
Do have software interrupts……
INT/ TRAP instructions
ring 0 系统
ring 1 OS
ring 2 设备驱动
ring 3 用户
和身份
身份实体，地址，属性

## Slide 19: Clocks and Timers
Real Time Clock (RTC)
  Returns encoding of current date
Programmable Interrupt Timer (PIT)
  Creates periodic event at set/ configurable interval
  Used to invoke periodic kernel tasks
  If frequency too
    Low: Kernel can seem unresponsive
    High: OS spends too much time servicing timer
1s运行千万次
格林威志时间：1970:01:01
周期性
低:内核可能看起来没有响应
高:操作系统花费太多时间维护计时器

## Slide 20: Avoiding Fine-grained Timers
Create an event queue: on timer interrupt…
  Set interval timer to time delta (+n ms) to next event
  Timer fires when next task due, rather than at set period
Technique used widely: OSs, simulators, etc.
细
我执行完你再执行

## Slide 21: Typical I/O Device
Circular buffers help improve data throughput
  Help decouple operation of processor and device
Status Register holds flags for
  Device ready
  Data available, etc.
循环缓冲器有助于提高数据吞吐量，帮助解耦处理器和设备的操作

## Slide 22: Direct Memory Access
Alternative to programmed I/O
Relieves CPU of data transfer
有cpu,可运行代码
大量数据从硬盘传到内存
cpu配置DMA
一条一条读
读完后向cpu发送中断说读完了，你可以处理了

## Slide 23: Managing I/O access within an Operating System
DEVICE DRIVERS

## Slide 24: Device Drivers
Uniform, defined interface to I/O system
  Unix adopted a common ‘file oriented’ interface read( ), write( ), ioctl( ), mmap( ), …
Extensible model
  Create new drivers as needed
  Loadable modules allow run-time changes
Drivers must typically be re-entrant
  Can be called again before previous request serviced
考试题
独立IO，IO映射
一致的
一开始没有启动，用什么，加载什么
可以重新进入

## Slide 25: Unix: Raw Device Entry Points
Entry point | Function
open( ) | Open the device
close( ) | Close the device
ioctl( ) | I/O control operations
mmap( ) | Map device contents into memory
read( ) | Input data
reset( ) | Reinitialise device
select( ) | Poll device for readiness
stop( ) | Stop output on device
write( ) | Output data

## Slide 26: Example device driver functions
Typically maintain table of device functions
Devices have NULL entries for functions/ operations that have no meaning for device
延时，匹配速度

## Slide 27: I/O in Traditional Unix Kernels
硬盘
磁盘
终端放硬盘
cache:cpu缓存
cooked:用户端缓存
未加密文件

## Slide 28: Unix I/O system in use
重新排序，更高效访问
解释数据（00101010->’a’)
硬盘
线解释器 八根线
数据库文件

## Slide 29: Device Driver Tasks
I/O Scheduling
Buffering, Spooling and Caching
Error Handling
I/O Protection
考试题
特权，改变顺序
buffer 在内存，一次性处理
脱机服务：将打印文件放进队列一个一个处理
cpu 有缓存
buffer与cache区别？

## Slide 30: Single- and Multi-Instance Devices
Single instance (e.g. a printer)
  Devices that can only be used by one process
  Error if another process attempts to use them
  – Often use spool files to sequence requests
Multi-instance
  Can handle requests from multiple sources
  Create another instance of internal data structures
单个实例(例如打印机)
只能被一个进程使用的设备
错误，如果另一个进程试图使用
它们经常使用spool文件对请求进行序列化
多实例
处理来自多个源的请求,多进程访问
创建内部数据结构的另一个实例

## Slide 31
Question？